Collaboration Document – Specification

# References
http://arduino.cc/en/Reference/HomePage
Arduino uses a language which has been derived from the popular processing programming environment. The above link provides a reference over the basic features.

# Weblinks
http://de.wikipedia.org/wiki/Relais#Halbleiterrelais
https://github.com/forflo/arduino_elsock (Link to repository)
http://arduino.cc/ (Homepage to Arduino)
http://arduino.cc/en/Reference/Ethernet (Reference for ethernet functionality)
http://arduino.cc/en/Tutorial/DhcpChatServer (Example code...)

# Material list
Electric cable capable of 220V alternating current
Surface mount housing

# Design

Arduino acts as controller and serves a static webpage which can be queried by sending requests like
GET / HTTP/1.1
[...]
This site contains n buttons (with n being the number of controllable electrical sockets) which can be clicked. Internally these buttons are just prettified hyperlinks.
GET /one HTTP/1.1
[…]

for example would thus result in a status change of the first electrical socket.

# Important notes
## Arduino hardware
IO-Ports just can handle 40mA of outgoing current. Any higher current would very likely damage the port or the ATMEGA chip.
Each port supplies 4,5V of voltage if used as output IO-Port.

The ATMEL-328P chips is used to power the Arduino-Ethernet.
# Firefox request
The following is an exact copy of the HTTP/1.1 request sended by the firefox webbrowser.
GET / HTTP/1.1
Host: 141.60.125.177
User-Agent: Mozilla/5.0 (Windows NT 6.1; rv:32.0) Gecko/20100101 Firefox/32.0
Accept: text/html,application/xhtml+xml,application/xml;q=0.9,*/*;q=0.8
Accept-Language: de,en-us;q=0.7,en;q=0.3
Accept-Encoding: gzip, deflate
Connection: keep-alive